## Slide 1: Part 3: Transport Layer

## Slide 2: Part 3: Transport Layer
Chapter goals:
Understand principles behind transport layer services:
  Multiplexing/demultiplexing
  Reliable data transfer
  Flow control
  Congestion control
Instantiation and implementation in the Internet
Chapter Overview:
Connection-oriented transport: TCP
  Reliable transfer
  Flow control
  Connection management
Principles of congestion control
TCP congestion control

## Slide 3: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
Full duplex data:
  Bi-directional data flow in same connection
  MSS: Maximum segment size
Connection-oriented:
  Handshaking (exchange of control msgs) inits sender, receiver state before data exchange
Flow controlled:
  Sender will not overwhelm receiver
Congestion control: To avoid network router buffer overflow
Point-to-point:
  One sender, one receiver
In-order byte steam:
  No “message boundaries”
Pipelined:
  TCP congestion and flow control set window size
Send & receive buffers
Reliable

## Slide 4: TCP
Transmission Control Protocol
Key Services:
  Send: Please send when convenient
  Data stream push: Destination TCP, please deliver it immediately to the receiving application.
  ⇒ Source TCP, please send it now.
  Set on last packet of an application message.
  Urgent data signaling: Destination TCP, please give this urgent data to the user out-of-band. Generally used for CTRL-C.

## Slide 5: TCP Segment Structure
Source port #
Dest port #
32 bits
Application
data
(variable length)
Sequence number
Acknowledgement number
Rcvr window size
Ptr urgent data
Checksum
F
S
R
P
A
U
Head
Len
Not
Used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK # valid
PSH: push data now
(Generally not used)
RST, SYN, FIN:
Connection establishment
(Setup, teardown cmds)
# Bytes
receiver willing
to accept
Counting by bytes of data
(not segments!)
Internet
Checksum
(As in UDP)
N.B: Every byte is numbered
Seq, ack are byte number
Pad

## Slide 6: TCP Header Fields
Source Port (16 bits): Identifies source user process
Destination Port (16 bits) 21 = FTP, 23 = Telnet, 53 = DNS, 80 = HTTP, ...
Sequence Number (32 bits): Sequence number of the first byte in the segment. If SYN is present, this is the initial sequence number (ISN) and the first data byte is ISN+1.
Ack number (32 bits): Next byte expected (got previous and expecting next)
Data offset (4 bits): Number of 32-bit words in the header
Reserved (6 bits)

## Slide 7: TCP Header Fields (Cont.)
Control (6 bits): Urgent pointer field significant,
  Ack field significant,
  Push function,
  Reset the connection,
  Synchronize the sequence numbers,
  No more data from sender
Window (16 bits): Will accept [Ack] to [Ack]+[window]-1
N. B.Byte number not packet or other
ACK is always 1 step ahead

## Slide 8: TCP Header Fields (Cont.)
Checksum (16 bits): covers the segment plus a pseudo header. Includes the following fields from IP header: source and dest adr, protocol, segment length. Protects from IP misdelivery. (initially TCP and IP were one protocol) (layering violation here)
Urgent pointer (16 bits): Points to the byte following urgent data. Lets receiver know how much data it should deliver right away out-of-band. (out of order)
Options (variable): Max segment size (does not include TCP header, default 536 bytes), Window scale factor, Selective Ack permitted, Timestamp, No-Op, End-of-options

## Slide 9: TCP Header Fields (Cont.)
T-L-V format
End of Options: Stop looking for further option
No-op: Ignore this byte. Used to align the next option on a 4-byte word boundary
Max Segment Size (MSS): Does not include TCP header
1b
1b

## Slide 10: TCP Header Fields (Cont.)
Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the TCP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
Checksum field is filled with zeros initially
TCP length (in octet) is not transmitted but used in calculations.
Efficient implementation in RFC1071.

## Slide 11: TCP Header Fields (Cont.)
Connection Establishment
  Three way handshake
  SYN flag set ⇒ Request for connection
Connection Termination q
  Close with FIN flag set
  Abort
ISN=Initial Sequence Number

## Slide 12: TCP Sequence #s and ACKs
Seq. #’s:
  Byte stream “number” of first byte in segment’s data
ACKs:
  Seq. # of next byte expected from other side
  Cumulative ACK
Q: How does receiver handle out-of-order segments?
  A: TCP spec doesn’t say, up to implementer
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
Host ACKs
receipt
of echoed
‘C’
Host ACKs
receipt of
‘C’, echoes
back ‘C’
time
Simple Telnet Scenario

## Slide 13: TCP ACK Generation [RFC 1122, RFC 2581]
Event
In-order segment arrival,
no gaps,
everything else already ACKed
In-order segment arrival,
no gaps,
one delayed ACK pending
Out-of-order segment arrival
higher-than-expect seq. #
gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver Action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single
cumulative ACK
Send duplicate ACK, indicating seq. #
of next expected byte
Immediate ACK if segment starts
at lower end of gap

## Slide 14: TCP: Retransmission Scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
time
Lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
Host A
Seq=100, 20 bytes data
ACK=100
Seq=92 timeout
time
Premature timeout,
cumulative ACKs
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=100 timeout
ACK=120

## Slide 15: RTT
The network must have buffers (to enable statistical multiplexing)
The buffer occupancy is time-varying
  As flows start and stop, congestion grows and decreases, causing buffer occupancy to increase and decrease.
RTT is time-varying. There is no single RTT.
Solution: make RTO a function of a smoothed RTT
buffers

## Slide 16: Smooth RTT
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125

## Slide 17: TCP Round Trip Time and Timeout
Setting the timeout (RTO)
RTO = EstimtedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
first estimate of how much SampleRTT deviates from EstimatedRTT:
RTO = EstimatedRTT + 4*DevRTT
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
Then set timeout interval:

## Slide 18: TCP Round Trip Time and Timeout
RTO = EstimatedRTT + 4*DevRTT
Might not always work
RTO = max(MinRTO, EstimatedRTT + 4*DevRTT)
MinRTO = 250 ms for Linux
500 ms for windows
1 sec for BSD
So in most cases RTO = minRTO
Actually, when RTO>MinRTO, the performance is quite bad; there are many spurious timeouts.
Note that RTO was computed in an ad hoc way. It is really a signal processing and queuing theory question…

## Slide 19: TCP Round Trip Time and Timeout
Setting the timeout
EstimatedRTT plus “safety margin”
Large variation in EstimatedRTT needs larger safety margin
Exponential weighted moving average
Influence of given sample decreases exponentially fast
Typical value of x: 0.1

## Slide 20: Principles of Congestion Control
Congestion:
Informally: “too many sources sending too much data too fast for network to handle”
Different from flow control!
Manifestations:
  Lost packets (buffer overflow at routers)
  Long delays (queueing in router buffers)
Top-10 problem!

## Slide 21: Causes/Costs of Congestion: Scenario 1
Two senders, two receivers
One router, infinite buffers
No retransmission
Large delays when congested
Maximum achievable throughput

## Slide 22: Causes/Costs of Congestion: Scenario 2
One router, finite buffers
Sender retransmission of lost packet

## Slide 23: Approaches Towards Congestion Control
End-end congestion control:
No explicit feedback from network
Congestion inferred from end-system observed loss, delay
Approach taken by TCP
Network-assisted congestion control:
Routers provide feedback to end systems
  Single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  Explicit rate sender should send at
Two broad approaches towards congestion control:

## Slide 24: TCP Congestion Control (1)
End-end control (no network assistance)
Transmission rate limited by congestion window size, cwnd, over segments:
w segments, each with MSS bytes sent in one RTT:
cwnd

## Slide 25: TCP Congestion Control (2)
“Probing” for usable bandwidth:
  Ideally: transmit as fast as possible (cwnd as large as possible) without loss
  Increase cwnd until loss (congestion)
  Loss: decrease cwnd, then begin probing (increasing) again
Two “phases”
  Slow start
  Congestion avoidance
Important variables:
  cwnd
  ssthresh: defines threshold between two slow start phase, congestion control phase

## Slide 26: Approaches towards congestion control
two broad approaches towards congestion control:
end-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate for sender to send at

## Slide 27: Case study: ATM ABR congestion control
ABR: available bit rate:
“elastic service”
if sender’s path “underloaded”:
  sender should use available bandwidth
if sender’s path congested:
  sender throttled to minimum guaranteed rate
RM (resource management) cells:
sent by sender, interspersed with data cells
bits in RM cell set by switches (“network-assisted”)
  NI bit: no increase in rate (mild congestion)
  CI bit: congestion indication
RM cells returned to sender by receiver, with bits intact

## Slide 28: Case study: ATM ABR congestion control
two-byte ER (explicit rate) field in RM cell
  congested switch may lower ER value in cell
  senders’ send rate thus max supportable rate on path
EFCI bit in data cells: set to 1 in congested switch
  if data cell preceding RM cell has EFCI set, receiver sets CI bit in returned RM cell
RM cell
data cell

## Slide 29: TCP Slow Start
Exponential increase (per RTT) in window size (not so slow!)
Loss event: timeout (Tahoe TCP) and/or or three duplicate ACKs (Reno TCP)
Host A
one segment
RTT
Host B
time
two segments
four segments
Notes: \begin{algorithm}
\caption{TCP Slow Start}
\begin{algorithmic}[1]
\STATE{Initialization: $cwnd \leftarrow 1$}
\REPEAT
\FOR{each segment ACKed}
\STATE{$cwnd \leftarrow cwnd + 1$}
\ENDFOR
\UNTIL{loss event or $cwnd > threshold$}
\end{algorithmic}
\end{algorithm}

## Slide 30: Slow Start Congestion Control
Initially SSThresh=Receiver window size
If segments lost, remember slow start threshold. SSThresh= CWND/2
Set CWND =1 MSS
Increment by 1MSS per ack until SSThresh
Increment by 1 MSS*MSS/CWND per ack afterwards
Congestion Window CWND
1MSS
bytes
Notes: \begin{algorithm}
\caption{TCP Slow Start}
\begin{algorithmic}[1]
\STATE{Initialization: $cwnd \leftarrow 1$}
\REPEAT
\FOR{each segment ACKed}
\STATE{$cwnd \leftarrow cwnd + 1$}
\ENDFOR
\UNTIL{loss event or $cwnd > threshold$}
\end{algorithmic}
\end{algorithm}

## Slide 31: TCP Congestion Avoidance
* TCP Reno skips slow start (fast
recovery) after three duplicate ACKs
Notes: \begin{algorithm}
\caption{TCP Congestion Avoidance}
\begin{algorithmic}[1]
\STATE{// Slow start is over; $cwnd > threshold$}
\REPEAT
\FOR{every $w$ segments ACKed}
\STATE{$cwnd \leftarrow cwnd + 1$}
\ENDFOR
\UNTIL{loss event}
\STATE{$threshold \leftarrow cwnd/2$}
\STATE{$cwnd \leftarrow 1$}
\STATE{Perform slow start$^{*}$}
\end{algorithmic}
\end{algorithm}

## Slide 32: Fast Retransmit and First Recovery
Optional – implemented in TCP Reno
(Earlier version was TCP Tahoe)
Duplicate Ack indicates a lost/out-of-order segment
On receiving 3 duplicate acks (4th ack for the same segment):
Enter Fast Recovery mode
Retransmit missing segment
Set SSThresh=CWND/2
Set CWND=SSThresh+MSS (some CWND=SSThresh+3 MSS)
Every subsequent duplicate ack: CWND=CWND+1MSS
When a new ack (not a duplicate ack) is received
Exit fast recovery
Set CWND=SSTHRESH

## Slide 33
Time out
3 dup ack

## Slide 34: TCP Reno
3 dup ack
Fast Retransmit
Fast Recovery
Time out
Slow start

## Slide 35: AIMD principal
Additive Increase, Multiplicative Decrease
Lets two users, using same link with capacity, C
W1 is the window of user 1, w2 is the window of user 2, and
W1+W2 = Capacity ⇒ Efficiency, W1=W2 ⇒ Fairness
(W1,W2) to (W1+ΔW,W2+ΔW) ⇒ Linear increase (45° line)
(W1,W2) to (kW1,kW2) ⇒ Multiplicative decrease (line through origin)
Fairness: everyone gets fair share
Efficiency; network resources are
used well
Notes: \begin{algorithm}
\caption{TCP Congestion Avoidance}
\begin{algorithmic}[1]
\STATE{// Slow start is over; $cwnd > threshold$}
\REPEAT
\FOR{every $w$ segments ACKed}
\STATE{$cwnd \leftarrow cwnd + 1$}
\ENDFOR
\UNTIL{loss event}
\STATE{$threshold \leftarrow cwnd/2$}
\STATE{$cwnd \leftarrow 1$}
\STATE{Perform slow start$^{*}$}
\end{algorithmic}
\end{algorithm}

## Slide 39: TCP Fairness
Fairness goal: if N TCP sessions share same bottleneck link, each should get 1/N of link capacity
TCP congestion avoidance:
AIMD: Additive increase, multiplicative decrease
  Increase window by 1 per RTT
  Decrease window by factor of 2 on loss event
AIMD
TCP connection 1
Bottleneck
router
capacity C
TCP
connection 2

## Slide 40: Why is TCP Fair?
Two competing sessions:
Additive increase gives slope of 1, as throughout increases
Multiplicative decrease decreases throughput proportionally
R
R
Equal bandwidth share
Connection 1 throughput
Connection 2 throughput
Congestion avoidance: additive increase
Loss: decrease window by factor of 2
Congestion avoidance: additive increase
Loss: decrease window by factor of 2

## Slide 41: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!

## Slide 42: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec

## Slide 43: TCP Average Throughput
Average Throughput=
Here, P = Probability of Packet loss

## Slide 44: Explicit Congestion Notification (ECN)
Explicit congestion notification (ECN) is based on DECbit.
Two bits in IP Header:
00: Transport is not capable of ECN (e.g., UDP)
01: Transport is capable of ECN
10: Transport is capable of ECN
11: Congestion experienced (CE)
When a router encounters congestion, instead of dropping the
datagram, it marks the two bits as “11” congestion experienced

## Slide 45: ECN (Cont)
On receiving “CE” code point, the receiver sends “ECN Echo (ECE)” flag in the TCP header
On seeing the ECE flag, the source reduces its congestion window, and sets “Congestion Window Reduced (CWR) flag in outgoing segment
On receiving “CWR” flag, the receiver, stops setting ECE bit

## Slide 46: TCP Futures: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L

## Slide 47: Summary
Principles behind transport layer services:
  Multiplexing/demultiplexing
  Reliable data transfer
  Flow control
  Congestion control
Instantiation and implementation in the Internet
  UDP
  TCP
Next:
Leaving the network “edge” (application transport layer)
Entering the network “core”

## Slide 48: Extra Slide

## Slide 49: Slow Start Congestion Control
At the beginning, SSThresh = Receiver window
After a long idle period (exceeding one round-trip time), reset the congestion window to one.
If CWND is W MSS, W acks are received in one round trip.
Below SSThresh, CWND is increased by 1MSS on every ack ⇒ CWND increases to 2W MSS in one round trip ⇒ CWND increases exponentially with time. Exponential growth phase is also known as “Slow start” phase
Above SSThresh, CWND is increased by MSS/CWND on every ack ⇒ CWND increases by 1 MSS in one round trip ⇒ CWND increases linearly with time The linear growth phase is known as “congestion avoidance” phase
Notes: \begin{algorithm}
\caption{TCP Slow Start}
\begin{algorithmic}[1]
\STATE{Initialization: $cwnd \leftarrow 1$}
\REPEAT
\FOR{each segment ACKed}
\STATE{$cwnd \leftarrow cwnd + 1$}
\ENDFOR
\UNTIL{loss event or $cwnd > threshold$}
\end{algorithmic}
\end{algorithm}