## Slide 1: ENGINEERING MANAGEMENT
CSE 417 Section 15/AB Term II
Session 2017-18
Department of Computer Science and Engineering
Instructor: Arif S. Bhuiyan, MSEd

## Slide 2: Chapter 5
Facility Location & Plant Layout

## Slide 3: Chapter Outline – Part I
Introduction
Facility Location Concepts
Factors affecting Facility Location
Facility Location Model
Facility Locations – Urban vs. Rural
Location Break-even Analysis

## Slide 4: Chapter Outline – Part II
Plan Layout
Objectives of Plant Layout
Principles of Plant Layout
Procedures in Planning the Layout
Plant Layout Tools and Techniques
Factors Influencing Plant Layout
Types of and Comparison of Plant Layout

## Slide 5: 3 Different Aspects of Facility Location are:
Selection of a Region
Selection of a Locality
Selection of a Site

## Slide 6: Why these aspects are critical?
Selection of a Region
Availability of raw materials
Nearness to the source
Proximity to the market
Availability of transportation facilities
Suitability of climate

## Slide 7: Why these aspects are critical?
Selection of Locality
Supply of labor
Prevailing wage rates
Existence of supplementary/complementary industries
Banking, credit, and communication facilities
Attitude of the local people
Local taxes and laws
Living conditions for workers
Water supply and fire-fighting services

## Slide 8: Why these aspects are critical?
Selection of a Site
Price of the land
Disposal of waste

## Slide 9: Factors Affecting Facility Location – page 121
Fundamental factors that should be considered in deciding location of facilities:
Demography - attitude of local population towards industrialization, expectations, adequate supply of labor of different skills and competitive price.
Land – cost of land and its development, support, availability for expansion, and surroundings
Incentives – Government provided incentives such as tax exemption, loans, subsidies, etc.
Government Regulations – additional subsidies, laws related to environmental protection, construction, waste disposal and safety laws.

## Slide 10: Factors Affecting Facility Location – page 121 (cont’d)
Fundamental factors that should be considered in deciding location of facilities:
Climate Conditions – subsoil water, humidity, local climate, etc.
Information related to Location – adequate land availability for present and future requirements (construction and expansion).

## Slide 11: Facilities Location in Urban Area
Advantages
Well connected (by rail, road and air)
Easy access pf experts and specialists
Availability of right labor force
Good facilities (hospitals, marketing, schools, banks, etc.)
Safe to work
Disadvantage
Limited availability of land
Cost of land and construction are high
High labor cost and local taxes
High costs for consumer goods
Labor union issues
Not too many sites are available

## Slide 12: Facilities Location in Rural Areas (Small Towns)
Advantages
Easy availability of land and cheap
Local laws are not so strict
Low taxes, insurance, etc.
Government incentives are available
No labor union issues
Healthy surroundings
Less risk and labor turnover
Disadvantage
Less availability of skilled labor
Poor communication and inadequate transportation
Inadequate power availability
Poor facilities and lack of specialized services
Non-availability of big market

## Slide 13: The economic comparison of location alternative is facilitate by the use id cost volume profit analysis known as location break-even analysis. The analysis can be done numerically/graphically. Following steps are involved in the break-even analysis: a. Determine the fixed and variable costs associated with each location alternative. b. Draw the total cost lines for all locational alternatives on the same graph c. Determine the location having the lowest total cost for the expected level of output
Location Break-even Analysis

## Slide 14: Assumptions a. Fixed costs are constant for the range of probable output b. The required level of output can be closely estimated c. Only one product is involved
Location Break-even Analysis

## Slide 15: Example#1 Gazipur, Daudkandi and Sylhet are the three potential locations for producing telecommunication set expected to sell for Tk. 90. Find the most economical location for an expected volume of 1850 units/year.
Location Break-even Analysis
Sites | Fixed cost/year | Variable cost/unit
Gazipur | 20,000 | 50
Daudkandi | 40,000 | 30
Sylhet | 80,000 | 10

## Slide 16: Steps: 1. Calculate the total cost Total Cost = Fixed Cost + Variable Cost Total cost at Gazipur = 20,000 + (50x1850) = 1,12,500 Total cost at Daudkandi = 40,000 + (30x1850) = 95,500 Total cost at Sylhet = 80,000 + (10x1850) = 98,500 2. Draw the cost volume graph 3. Calculate expected Profit Expected Profit = Total Revenue – Total Cost Expected Profit at Gazipur = (90x1850) – 1,12,500 = 54,000/yr Expected Profit at Daudkandi = (90x1850) – 95,500 = 71,000/yr Expected Profit at Sylhet = (90x1850) – 98,500 = 68,000/yr
Let’s Calculate – page 126

## Slide 17: Cost Volume Graph
120
80
40
2000
1000
3000
Annual Volume, Unit
Annual Cost

## Slide 18: Plant Layout
“Plant Layout means placing the right equipment coupled with the right methods in the right place to permit the processing of product(s) in the most effective manner through the shortest move in shortest time.”
Thorough knowledge of the following factors is essential:

## Slide 19: An Efficient Layout
Flow of production
Utilization of Space available
Easy flow of materials, workers and machines
Minimum handling of one operation to the next
Appropriate facilities to safeguard the health of workers
Convenient location for store
Safety of workers under the provision of Factories Act

## Slide 20: An Efficient Layout
Adequate inter-departmental space
Effective coordination and integration among men, machine and materials for maximum utilization
Facilitation of supervision, coordination and control by workers
Capability of incorporating changes in the management policies