## Slide 1: Optical Reading Mechanism

## Slide 2: Optical Positioning
The beam must maintain focus to with the size of pits or beams on the surface
The beam should follow track precisely

## Slide 3: Optical Positioning
There are two aspects to the positioning of the laser beam when reading data optically
  Focus control
  Track following
  Focus control:
  Focusing of laser beam on the surface depends on
  the distance between objective lens and the surface

## Slide 4
In order to provide the required depth of focus
    Sensors must be arranged such that, one sensor is actually four separate sensors arranged in a diamond shape
    A cylindrical lens is placed between beam splitter and sensor array
        Alters the shape of the cylindrical laser beam
        When in focus- appears as a circle on the sensor array
        When out of focus- appears as elliptical image on the sensor array
  The output of the top and bottom sensors is summed and compared with the output sum of the left and right sensors

## Slide 5: Focus control

## Slide 6: Track Following

## Slide 7: Bar Codes
Any situation in which a machine readable identification is required may make use of a suitable bar code
handheld barcode scanner
Barcode

## Slide 8: Benefits of Bar Coding
Represent unique identity of a product
Aid effective management of resources and inventories
Labor savings by avoiding manual system
Cost efficient

## Slide 9: Bar Code Scanners
barcode reader (or barcode scanner) is an electronic device for reading printed barcodes
Bar Code symbol consists of series of vertical dark bars separated by light spaces
When illuminated reflected light is detected by electro optical sensor
The intensity of reflected light from the dark bars is less than that of spaces

## Slide 11: CCD(Charge Coupled Device) Scanner arrangement

## Slide 12: Codes
UPC (Universal Product Coding)
  Prefix – 1 digit
  Manufacturer number- 5 digits
  Item reference – 5 digits
  Check digit – 1 digit
EAN (European Article Number)
  Prefix – 2 digits
  Manufacturer number- 5 digits
  Item reference – 5 digits
  Check digit – 1 digit
Checksum Calculation?
12 Digits
13 Digits